## Slide 1: Common Emitter Amplifier
by:
Cole Bailey (SID: 014346785)
Paco Ellaga (SID: 009602331)
Jahaira Lucas (SID: 013989155)
Donovan Minto (SID: 013881580)

## Slide 2: Objective
Design an NPN configured Common Emitter (CE) Amplifier
Determine the results of the following:
  Mid - frequency gain, AMID-FREQ,
  Low frequency poles, FL,
  High frequency poles, FH,
Understand real-world applications of the CE Amplifier

## Slide 3: Design & Characteristic Results
Coupling Capacitors
  C1 and C3 blocks DC
Bypass Capacitor
  RE increases gain in the circuits midband frequencies
  Decreases bandwidth (shown in images)
Use T-model of the BJT to create an equivalent circuit
Set Vin = 0 to get 3 individual circuits to find the time constants of each capacitor

## Slide 4: Design & Characteristic Results
Low Frequency poles = inverse of capacitor time constants
Image 1: Frequency response of the CE Amplifier with the bypass capacitor
  Gain = 41 V/V
  Lower 3dB cutoff frequency = 225 Hz
  Upper 3dB cutoff frequency = .93 MHz
Image 2: Frequency response after removing the bypass capacitor
  Gain = 1.8 V/V
  Lower 3dB cutoff frequency = 100 Hz
  Upper 3dB cutoff frequency = 3.5 MHz
fH = 1 / (2π*Cin*R’SIG )

## Slide 5: Application #1
RF modules
  Transmitter, receiver, transceiver, and System on a Chip (SoC)
Electronic wireless communication systems
Monitoring systems
  Can be used in city and county law enforcement
  Able to track defendants through ankle bracelet and a monitoring base station
Smart-Technology Devices
  Smart door locks
  Bluetooth trackers
  Home audio systems

## Slide 6: Application #2
Low-noise amplifiers (LNA)
  Takes low powered signals and amplifies them without affecting signal-to-noise ratio
Signal-to-Noise Ratio (SNR)
  Ratio of power of signal to power of noise
  SHould be greater than 1:1
Used to amplify signal and reduce noise in the receiver
  Placing LNA closer to signal source (top of antenna), reduces noise by the gain provided from LNA
CE configuration yields medium source impedance

## Slide 7: Conclusion
The CE amplifier can be implemented in numerous applications
Most relevant application is in RF and wireless communication systems
Transistor amplifiers (CE, CS, CD, etc.) can be configured in different ways and each has a different application

## Slide 8: THANK YOU!